## Slide 1: Computer Fundamentals
Dr. Safdar Nawaz Khan Marwat
DCSE, UET Peshawar
Lecture 10

## Slide 2: Outline
Modern CPUs

## Slide 3: Intel 4004
The 1st commercially available microprocessor
Introduced in 1971
4-bit CPU
2250 transistors
740 kHz max clock rate
Packaged in 16-pin ceramic package
As powerful as ENIAC
  Which had 18000 vacuum tubes and occupied a large room
Targeted use: Calculators
Cost: less than $100
Source: https://www.linkedin.com/pulse/intel-4004-italian-job-edoardo-piccari

## Slide 4: Intel 4004 (cont.)
Busicom, Japanese calculator manufacturer
  Demanded from Intel to develop 16 separate IC’s
  For a line of new calculators
Chief designers
  Federico Faggin
  Ted Hoff
  Masatoshi Shima
Intel known only as memory manufacturer at that time
  Was quite small
  Lacked resources to do all 16 chips
Ted Hoff came up with the idea
  Do all 16 on a single chip
Later realized that 4004 could have other uses

## Slide 5: Intel Pentium IV
Introduced in December 2001
Single core CPU
55 million transistors
32-bit processor
2 ALU’s
3.8 GHz max clock rate
For PC’s and low-end workstations
Introductory cost: around $600
Source: https://www.amazon.com/Intel-Pentium-2-6Ghz-SL6PP-Socket/dp/B004NKB7GE

## Slide 6: Moore’s Law
Gordon Moore, one of the founders of Intel
  Predicted that
    The number of transistors on an IC OR the capability of microprocessors
    Will double every year
  Later modified it to 18 months
Still holds true
In fact, time required for doubling is contracting
  Closer to a year now

## Slide 7: Moore’s Law (cont.)

## Slide 8: Koomey’s Law
https://www.extremetech.com/computing/95913-koomeys-law-replacing-moores-focus-on-power-with-efficiency

## Slide 9: Metcalfe’s Law
https://en.wikipedia.org/wiki/Metcalfe%27s_law

## Slide 10: Big O Notation

## Slide 11: Word Length
4004 dealt with data in chunks (words) of 4-bits at a time
Pentium IV deals with data in chunks of 32-bit length
New processors deal with 64-bit chunks at a time

## Slide 12: Clock Frequency
4004 worked at a clock frequency of 740 kHz
Pentium IV worked at 3.8 GHz
Latest processors have clock frequencies in GHz
Higher clock frequency results in more power
  If both processors have same design
  Example: PowerPC & Pentium 4 microprocessors at same frequency
    Former performs better due to superior design

## Slide 13: Enhancing Performance
Computing capability of microprocessor
Can be enhanced in different ways
  By increasing clock frequency
  By having a more effective caching algorithm and the right cache size
  By adding more functional units (e.g. ALU’s, FPU’s etc.)
  Improving architecture (registers, bus etc.)

## Slide 14: Looking Inside the Processor
Architecture
  Determines
    Location of CPU parts
    Word size
    Number of registers
    Pipelines
  Main difference between CPUs
Notes: Teaching tip
Bit size tends to confuse students. A simple example clarifies the importance of bit size. Consider two equal computers, one has a 32-bit processor, the other a 64 bit processor. With all other items equal, the 64-bit processor will handle twice the data the 32 bit processor handles. This is like driving a car at 55 Mph then doubling it to 110 Mph.

## Slide 15: Microcomputer Processors
Intel
  Leading manufacturer of processors
  Intel 4004 was worlds first commercial microprocessor
  IBM PC in 80s powered by Intel 8088
  Well known Intel processors
    Centrino
    Itanium
    Pentium IV
    Xeon
    Core i7

## Slide 16: Microcomputer Processors (cont.)
Advanced Micro Devices (AMD)
  Main competitor to Intel
  Originally produced budget products
  Current products outperform Intel
  Designed processors
    Sempron
    Athlon FX 64
    Athlon XP

## Slide 17: Microcomputer Processors (cont.)
Freescale
  A subsidiary of Motorola
    Apple computers primarily have Freescale
  Currently focuses on Linux market
IBM
  Historically manufactured mainframes
  Series of high performance microprocessor called POWER
    Performance Optimization With Enhanced RISC (POWER)
    Named as POWER1, POWER2, up to recent POWER9
Notes: IBM also manufactures for Apple

## Slide 18: Comparing Processors
Frequency of processor
Size of cache
Word size
Speed of system bus

## Slide 19: Advanced Processor Topics
RISC processors
  Reduced Instruction Set Computing
  Smaller instruction sets
    May process data faster
    Processor capable of executing those instructions using fewer cycles
  IBM Power, iPhone, iPad and several Android based-systems
Parallel Processing
  Multiple processors in a system
    Computational task is broken down in several subtasks
    Processed independently
  Symmetric Multiple Processing (SMP)
    Processors share common memory
    Number of processors preferably a power of 2 (divide and crush)
  Massively Parallel Processing
    Thousands of processors
    Mainframes and super computers
Notes: opposing architecture is called complex instruction set computing (CISC)

## Slide 20: Extending Processors Power
Standard computer ports
  Keyboard and mouse ports
  USB ports
  Parallel
  Network
  Modem
  Audio
  Serial
  Video

## Slide 21: Extending Processors Power (cont.)
Serial and parallel ports
  Connect to printers or modems
  Parallel ports move bits simultaneously
    Made of 8 – 32 wires
    Internal busses are parallel
  Serial ports move one bit
    Lower data flow than parallel
    Requires wires for control and ground purposes
  Universal Asynchronous Receiver/Transmitter (UART)
    Converts from parallel to serial and vice versa
  Why USB based on serial architecture?
    Assignment 1.

## Slide 22: Serial Communications
Notes: UART: Universal Asynchronous Receiver/Transmitter

## Slide 23: Parallel Communications

## Slide 24: Extending Processors Power (cont.)
SCSI
  Small Computer System Interface
    Set of standards
    Physical connection between computers and peripheral devices
    For transferring data
  Supports dozens of devices
  External devices daisy chain
  Fast hard drives and CD-ROMs
USB
  Universal Serial Bus
  Most popular external bus
  Supports up to 127 devices
  Hot swappable
FireWire
  IEEE 1394
  Cameras and video equipment
  Hot swappable
  Port is very expensive

## Slide 25: Specialized Expansion Ports
Expansion slots and boards
  Allows users to configure machine
  Slots allow addition of new devices
  Devices are stored on cards
  Computer must be off before inserting
PC Cards
  Expansion bus for laptops
  Standardized by PCMCIA
    Personal Computer Memory Card International Association
  Hot swappable
  Small card size
  Three types
    I for memory
    II for network adapters
    III for hard drives
Plug and play
  New hardware detected automatically
  Prompts to install drivers
  Non-technical users can install devices
Notes: Insider Information
Plug and play was introduced by Apple Computers.

## Slide 26: Microcontrollers
A type of microprocessor systems
Not very powerful, not expensive
Found embedded in
  Video games
  VCRs
  Microwave ovens
  Printers
  Autos, etc.
Complete CPU on a chip
Direct input/output capability and memory
Specialized application-specific components
More than 90% of the microprocessors are microcontrollers
  Manufactured for embedded computing applications
  In 2000, 365 million microprocessors and 6.4 billion microcontrollers manufactured