## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.1 The MSP430 Digital I/O System

## Slide 2: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
Digital I/O
=
Parallel Ports
P1, P2, P3, P4, P5, P6
PA=P1:P2
PB=P3:P4
PC=P5:P6

## Slide 3: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
Recall that the MCUs share functionality on pins in order to reduce the size and cost of the device.

## Slide 4: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
Image Courtesy of
Recording Connection of Canada
This figure shows the details of the MCU digital I/O breakout on the LaunchpadTM

## Slide 5: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.1 Configuration Registers
Peripherals are setup and interfaced with using registers within the memory map.
Bit Set and Bit Clear instructions are used to configure the registers.

## Slide 6: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.1 Configuration Registers – Documentation
The MSP430FRxx Family User’s Guide gives the name and purpose of each register.

## Slide 7: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.1 Configuration Registers – Documentation
The MSP430 Device Specific Datasheet gives the details of which peripherals are available, which pin they are on, and how to select the function.

## Slide 8: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.1 Configuration Registers – Documentation
The LaunchPad Development Kit User’s Guide tells where the I/O are connected on the red board.

## Slide 9: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.1 Port Direction Registers (PxDIR)
The port direction registers dictate whether the port bits are configured as inputs or outputs.
The logic for PxDIR is as follows:
  Bit = 0: Pin is an input (default)
  Bit = 1: Pin is an output
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 10: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.2 Port Input Registers (PxIN)
Image Courtesy of
Recording Connection of Canada
Each bit within PxIN registers represent the logic levels at the input signals pins.
Bit = 0: Logic low Bit = 1: Logic high
Read only registers
In order to read from an input port bit, a program can either move the information into a CPU register, or do bit compares on the PxIN memory location.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 11: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.3 Port Output Registers (PxOUT)
Image Courtesy of
Recording Connection of Canada
Each bit within the PxOUT registers is the value to be output to the port’s signal pin when the bit is configured to be an output.
In order to write to an output port bit, a program can move information into the PxOUT register, or perform bit set/clear operations on the PxOUT address location.
When a port bit is configured as an input, the PxOUT register has a secondary role, which is to dictate the polarity of an optional pull-up/down resistor.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 12: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.4 Port Pullup/Pulldown Register Enable Registers (PxREN)
Image Courtesy of
Recording Connection of Canada
If a port is an input, an optional pull-up or pull-down resistor can be attached.
The bits within PxREN control the corresponding bit location within PxIN.
The resistor resides in the MCU.
Bit = 0: Disabled Bit = 1: Enabled
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Gnd

## Slide 13: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.4 Port Pullup/Pulldown Register Enable Registers (PxREN)
Pull-up and pull-down resistors are typically very large (10kΩ → 1MΩ) so that external circuitry can easily override them.
But the pull-up resistors are “just” strong enough that when nothing is driving the pin, it will pull them to a known logic level (HIGH or LOW).
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Gnd

## Slide 14: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.4 Port Pullup/Pulldown Register Enable Registers (PxREN)
To configure whether the resistor is a pull UP or pull DOWN, the PxOUT register is used. PxOUT = 0: Resistor is a Pull Down PxOUT = 1: Resistor is a Pull Up
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Gnd

## Slide 15: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.4 An Example of Using the Pull Up/Down Resistors
Single-pole, single-throw (SPST) switch/button – simplest form of a switch, one input and one output
When the switch is open, the input and output are not connected.
When the switch is closed, the input and output are connected.

## Slide 16: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.4 An Example of Using the Pull Up/Down Resistors
Adding a pull-up resistor connected to the power supply can provide a logic high when the switch is open.
This takes two steps:
  PxREN = 1 (enable the resistor)
  PxOUT = 1 (make it a pull UP)

## Slide 17: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.5 Port Function Select Registers
(PxSEL1 and PxSEL0)
The Port Function Select (PxSEL) registers tell the MCU which function to use, including whether to make the signal pin a digital input/output.
PxSEL1 and PxSEL0 hold the two selection bit.
The function is found in the Device Specific Datasheet

## Slide 18: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.6 Digital I/O Enabling After Reset
Image Courtesy of
Recording Connection of Canada
The steps to fully set up a digital I/O for use can be summarized in the following steps:
  Initialize Configuration Registers: PxDIR, PxREN, PxOUT if applicable, and PxSEL1: PxSEL0.
  Clear the LOCKLPM5 bit in the PM5CTL0 register (low power, high-Z input mode by default)
  Your program may now start using the PxIN or PxOUT register.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 19: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.1 The MSP430 Digital I/O System
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 20: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.1 The MSP430 Digital I/O System – The MSP430.h Header

## Slide 21: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.7 Using Literal Definitions from the
MSP430.H Header File
To eliminate the need for the programmer to look up the absolute address of each register within the memory map, Code Composer Studio automatically includes a header file with literal names defined for the memory addresses.
Main header files we will use: msp430.h and msp430fr2355.h
These files contain the exact spelling of the register names and abbreviations of the memory map.
These register names are NOT address labels. They are simply name substitutions. So we need to use absolute addressing: i.e., bis.b #BIT0, &P1DIR

## Slide 22: Ch. 9: The MSP430 Digital I/O System
9.1 The MSP430 Digital I/O System
9.1.7 Using Literal Definitions from the
MSP430.H Header File

## Slide 23: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.1 The MSP430 Digital I/O System – The MSP430.h Header
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 24: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.2 Digital Output Programming
Image Courtesy of
Recording Connection of Canada

## Slide 25: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Digital Output Program
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Initialize Configuration Registers:
P1DIR bit 0 = 1 ;Configure P1.0 as an OUTPUT
Clear LOCKLPM5 in PM5CTL0 register
Using the names defined in the header file, the assembly code to accomplish this configuration is:
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 26: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Using a Digital Output to Drive LED1
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_Dig_IO_Outputs_n_LEDs
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 27: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Using a Digital Output to Drive LED1
Step 3: Debug your program.
Step 4: Set a breakpoint before the first instruction
bis.b #BIT0, P1DIR
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 28: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Using a Digital Output to Drive LED1
Step 5: Run your program to the breakpoint.
Step 6: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 29: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Tips and Tricks
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
The port registers may be viewed during the debug process.
When the digital I/O is not configured correctly, the result is that the I/O pin simply does nor work.
When this occurs, the only way to figure out what is going on is to go into the Register Viewer and make sure the configuration registers are set up as desired.

## Slide 30: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Viewing Port Registers in the Debugger
Step 1: Open the project from the last example titled Asm_Dig_IO_Outputs_n_LEDs. If you didn’t do the last example, create a new Empty Assembly-only CCS project of this name.
Step 2: If necessary, type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 31: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Viewing Port Registers in the Debugger
Step 3: Debug your program.
Step 4: Set a breakpoint before the first instruction
bis.b #BIT0, P1DIR
Step 5: Run to the breakpoint.

## Slide 32: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Viewing Port Registers in the Debugger
Step 6: Open the Register Viewer and scroll down.
Step 7: Expand the P1 register. You will see all of the configuration registers for this port and their current settings.
Step 8: Change the format to binary. Note that there are additional configuration registers for P1 that have not been covered yet.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 33: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Viewing Port Registers in the Debugger
Step 9: Step your program through the main loop and observe how P1.0 is set and cleared and how this corresponds to LED1 turning on and off.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 34: Ch. 9: The MSP430 Digital I/O System
9.2 Digital Output Programming
Example: Viewing Port Registers in the Debugger
Step 10: Now manually enter 1’s and 0’s for P1.0 in the P1OUT register.
Step 11: After each entry, hit return. Notice that LED1 turns on and off based on your entry. This is a helpful technique to ensure that the configuration registers are correct and that the LaunchPad™ is working as expected.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 35: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.2 Digital Output Programming
Image Courtesy of
Recording Connection of Canada
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 36: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.3 Digital Input Programming
Image Courtesy of
Recording Connection of Canada

## Slide 37: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
9.3 Digital Input Programming
There are two push-button switches provided on the LaunchPad™ board labeled S1(P4.1) and S2(P2.3).
Both push-button switches are SPST with their inputs connected to ground. This provides a logic LOW to the MCU when not pressed.
To use these switches, include pull-up resistors on the MCU to provide a known state when not pressed.

## Slide 38: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
9.3 Digital Input Programming
Polling - creating a program loop that will continually check the value of the input and only exit the loop if the value changes.

## Slide 39: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_Dig_IO_Inputs_n_Polling_S1
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 40: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1

## Slide 41: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1
Step 3: Debug your program.
Step 4: Run your program and test whether LED1 toggles when you press SW1.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 42: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
9.3 Digital Input Programming
The reason that LED1 is not always toggled when you press and release S1 is because you can never tell what value LED1 is at when you release the button.
The reason that LED1 appears dimmer when you hold down S1 is because it is being continually turning LED1 on and off millions of times each second while the program checks S1, exists the polling loop, and performs the XOR toggle operation.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 43: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
9.3 Digital Input Programming
Consider this new logic for polling S1 that inserts some delay after the LED1 toggling action.

## Slide 44: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1 with Delay
Step 1: Open the project form the last example titled:
Asm_Dig_IO_Inputs_n_Polling_S1
Step 2: Type in the delay portion of the code into the main.asm.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 45: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1 with Delay

## Slide 46: Ch. 9: The MSP430 Digital I/O System
9.3 Digital Input Programming
Example: Polling the Input S1
Step 3: Debug your program.
Step 4: Run your program and test whether LED1 toggles when you press SW1 more reliably than before.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 47: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 9: Digital I/O
9.3 Digital Input Programming
www.youtube.com/c/DigitalLogicProgramming_LaMeres